## Slide 1
Methodology for Using AEDT and MOVES for Airport Air Quality Analyses
George Noel
The National Transportation Systems Center
Advancing transportation innovation for the public good
U.S. Department of Transportation
Office of the Secretary of Transportation
John A. Volpe National Transportation Systems Center
108th Air & Waste Management Association Annual Conference and Exhibition
Paper # 81
June 24th, 2015

## Slide 2: Background - AEDT
Aviation Environmental Design Tool (AEDT) version 2b released May 29th, 2015
  Replaces Emissions and Dispersion Modeling System (EDMS) 5.1.4.1 (August 2013) as the preferred model for airport air quality analyses
  Replaces the Integrated Noise Model (INM)
  EPA’s MOtor Vehicle Emission Simulator (MOVES) is not embedded within AEDT 2b or EDMS 5.1.4.1
    EDMS: The Usage of the U.S. Environmental Protection Agency's (USEPA) Motor Vehicle Emission Simulator (MOVES) with the Federal Aviation Administration's (FAA) Emissions and Dispersion Modeling System (EDMS) (February 28th, 2014)
  AEDT 2b: Using MOVES with AEDT 2b Version 1.0
    Available on AEDT website: https://aedt.faa.gov/

## Slide 3: Background - MOVES
MOVES is required model for estimating emissions from on-road mobile sources
  Required as of March 2013
  Replaces MOBILE6.2
MOVES2014 is the current version
  Released October 7th, 2014
  Replaces MOVES2010b
  2 year grace period with exceptions
  NONROAD2008 embedded

## Slide 4: Background - EDMS
EDMS – Roadway Input Interface

## Slide 5: Using AEDT with MOVES
Emissions Inventories
  Analysts will generate emissions inventories for on-road and off-road (e.g. construction equipment) mobile sources independently of AEDT 2b
  Emissions Inventory results may be imported in AEDT 2b
    The following Emissions Inventory categories can be imported
      Roadways
      Parking Facilities
      Construction

## Slide 6: Using AEDT with MOVES
Dispersion Modeling
  Analysts will generate AERMOD input files for on-road and off-road (e.g. construction equipment) mobile sources independently of AEDT 2b
    Analyst generated AERMOD input file (.inp)
    Analyst generated AERMOD hourly emission rate file (.hre)
  AERMOD .inp and .hre files may be imported into AEDT 2b
    Merged with aircraft and other airport sources

## Slide 7: Methodology – MOVES
MOVES executed at Project Level Domain
  Allows for Link (roadway segment) level emissions estimates
Each MOVES run models a single hour
  Single hour, month, and year for each MOVES run
Number of MOVES runs required may vary
  Use Case
    Emission Inventory may require less runs
    Dispersion modeling may require more runs
  Meteorological variation
  Traffic Variation

## Slide 8: Methodology – MOVES
Number of MOVES Runs
  Determined by interagency coordination
Meteorological and traffic variation
  An example of a detailed set of runs is 16 MOVES runs
  Quarterly seasonal variation (Table 1)
  Daily traffic variation (Table 2)
Code | Name | Months
Q1 | First Quarter | January - March
Q2 | Second Quarter | April – June
Q3 | Third Quarter | July - September
Q4 | Fourth Quarter | October - December
Code | Name | Time of Day
AM | Morning Peak | 0600 – 0900 (3 hours)
MD | Midday | 0900 – 1600 (7 hours)
PM | Evening Peak | 1600 – 1900 (3 hours)
ON | Overnight | 1900 – 0600 (11 hours)
Table 1. Quarters of the year for MOVES runs
Table 2. Traffic volume times of day for MOVES runs

## Slide 9: Methodology – MOVES
Scale

## Slide 10: Methodology – MOVES
Pollutant | Emissions Process
Total Gaseous Hydrocarbons | Running Exhaust and Crankcase Running Exhaust
Non-Methane Hydrocarbons | 
Non-Methane Organic Gases | 
Volatile Organic Compounds | 
Total Organic Gases | 
Carbon Monoxide (CO) | 
Oxides of Nitrogen (NOX) | 
Sulfur Dioxide (SO2) | 
Total Energy Consumption | 
Atmospheric CO2 | 
Primary Exhaust PM10 - Total | 
Primary Exhaust PM2.5 - Total | 
Primary PM10 - Organic Carbon | 
Primary PM2.5- Organic Carbon | 
Primary PM10 - Elemental Carbon | 
Primary PM2.5 - Elemental Carbon | 
Primary PM10 - Sulfate Particulate | 
Primary PM2.5 - Sulfate Particulate | 
Primary PM10 - Brakewear Particulate | Running Exhaust, Crankcase Running Exhaust, and Brakewear
Primary PM2.5 - Brakewear Particulate | 
Primary PM10 - Tirewear Particulate | Running Exhaust, Crankcase Running Exhaust, and Tirewear
Primary PM2.5 - Tirewear Particulate | 
Pollutants and Processes for Roadway Links
  These Pollutants and processes must be selected so results appropriately map to AEDT

## Slide 11: Methodology – MOVES
Output – General Output
Notes: This table shows the emissions and fuel consumption rates association with each event that occurs during the inspection process.
The “Event Type” is one emissions component of the entire inspection process.

## Slide 12: Methodology – MOVES
Links
  Roadway Links
    Unique Link for each Roadway Segment
      Road Type
      Average Speed (mph)
      Length (miles)
      Grade (%)
  Parking Facility Links
    Three Links for each Parking Facility/Level
      Parking Facility Movement Link
      Idle Link
      Off-Network Link (starts and soak)
        Only a single off-network link can modeled with each MOVES run

## Slide 13: Methodology – MOVES Output
After all MOVES runs have been completed, the analyst will have generated output by each link represented in total grams of each pollutant for the hour modeled.
The MOVES output for all links is located in the “movesoutput” table within the output database.
The analyst must conduct post processing on the MOVES output so that pollutants match those generated by the other sources modeled with AEDT
Pollutant | MOVES Pollutant ID
THC | 1
CO | 2
VOC | 87
NMHC | 79
TOG | 86
NOx | 3
SOx | 31
PM10 | 100 (100 + 106 + 107)
PM2.5 | 110 (110 + 116 + 117)
CO2 Atmospheric | 90
H2O | 119

## Slide 14
Methodology – MOVES Output
AEDT accepts a comma separated file (.csv) for importing an emission inventory
A single emission inventory for each analysis year can be imported in AEDT
Four columns of information are to be included in the .csv import file
  YearID – Analysis Year
  Source – Roadway, Parking Facilities, and Construction
  PollutantID – MOVES Pollutant ID
  emissionQuant – total mass in grams
Example of Emissions Inventory Input File

## Slide 15
Methodology – AEDT Import
Emission Inventory and AERMOD input files Import

## Slide 16
Methodology – AERMOD Input Files
AEDT does not manage or utilize geospatial data associated with roadway links or parking facility links
  The analyst can import a GIS shape file (.shp) to display roadways on the AEDT map viewer.
    Shape file data is not used for any other purpose (e.g., AERMOD)
Analyst is responsible for managing geospatial coordinates of roadway and parking facility sources
  All AERMOD source coordinates are based on a local coordinate system with the origin based on the airport reference point
  UTM Coordinates are not utilized

## Slide 17
Methodology – AERMOD .inp File
Roadway Sources
  Modeled using AREA sources
Parking Sources
  Modeled using AERAPOLY sources
  Each level of a parking garage is to be modeled as an individual source
Construction Sources
  Can be modeled as AREA, AREAPOLY, POINT, or VOLUME sources

## Slide 18
Methodology – AERMOD .inp File
The analyst needs to only specify the CO and SO Pathways

## Slide 19
Methodology – AERMOD .hre File

## Slide 20
Methodology – AERMOD .inp and .hre Requirements
A minimum of one parking facility must be included in the .inp and corresponding .hre file. If the analyst does not want to model a parking facility then the emission rates can be set to zero in the .hre file.
The following naming conventions must be used in order for the AERMOD .inp to import correctly into AEDT.
  Parking Facilities: naming range of PARKA001 through PARKZ999
  Roadways: naming range of RD000001 through RD999999
  Construction: naming range of RDC00001 through RDC99999
The order of the sources listed under the SRCPARAM keyword in the .inp must be ordered in the following manner:
  All roadway sources are to be defined first.
  All construction sources are to be defined following the roadway sources.
  All parking facility sources are to be defined after the construction sources. If there are no construction sources to be modeled then the parking facility sources will follow the roadway sources. Construction Sources

## Slide 21
The POLLUTID in the CO (control) Pathway in the AERMOD input file must match the AEDT Metric Result being modeled. For example, if the CO (carbon monoxide) Metric is chosen to be modeled in AEDT then CO (carbon monoxide) must be listed with the POLLUTID keyword within the CO (control) Pathway section of the AERMOD input fileThe following naming conventions must be used in order for the AERMOD .inp to import correctly into AEDT.
The AERMOD input file (.inp) and the hourly emission rate file (.hre) must have the same naming convention. For example, if the AERMOD input file name is CO_airportXYZ.inp then the hourly emission rate file is to be named CO_airportXYZ.hre.
The order of sources in the hourly emission rate file (.hre) must be ordered in the following manner:
  All parking facility sources are to be listed first.
  All roadway sources are to be listed following the parking facility sources.
  All construction sources are to be listed following the roadway sources.
Methodology – AERMOD .inp and .hre Requirements

## Slide 22
AEDT Emissions Inventory Results

## Slide 23
AEDT Dispersion Analysis Results

## Slide 24
AEDT Dispersion Analysis Results

## Slide 25: Questions?
George Noel
Email: george.noel@dot.gov
AEDT Website
    https://aedt.faa.gov/